## Slide 1
Chapter 18
Introduction to
Network
Layer
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
Chapter 18: Outline
18.1 NETWORK-LAYER SERVICES
18.2 PACKET SWITCHING
18.3 NETWORK-LAYER PERFORMANCE
18.4 IPv4 ADDRESSES
18.5 FORWARDING OF IP PACKETS

## Slide 3
Chapter 18: Objective
The first section introduces the network layer by defining the services provided by this layer. It first discusses packetizing. It then describes forwarding and routing and compares the two. The section then briefly explains the other services such as flow, error, and congestion control.
The second section discusses packet switching, which occurs at the network layer. The datagram approach and the virtual-circuit approach of packet switching are described in some detail in this section.
Network-layer performance. We describe different delays that occur in network-layer communication. We also mention the issue of packet loss. Finally, We discuss the issue of congestion control at the network layer.

## Slide 4
Chapter 18: Objective (continued)
The fourth section discusses IPv4 addressing, probably the most important issue in the network layer. It first describes the address space. It then briefly discusses classful addressing, which belongs to the past but is useful in understanding classless addressing. The section then moves to classless addressing and explains several issues related to this topic. It then discusses DHCP, which can be used to dynamically assign addresses in an organization. Finally, the section discusses NAT, which can be used to relieve the shortage of addresses to some extent.
The fifth section discusses forwarding of network-layer packets. It first shows how forwarding can be done based on the destination address in a packet. It then discusses how forwarding can be done using a label.

## Slide 5
    18-1 NETWORK-LAYER SERVICES
Before discussing the network layer in the Internet today, let’s briefly discuss the network-layer services that, in general, are expected from a network-layer protocol. Figure 18.1 shows the communication between Alice and Bob at the network layer. This is the same scenario we used in Chapters 3 and 9 to show the communication at the physical and the data-link layers, respectively.

## Slide 6
Figure 18.1: Communication at the network layer

## Slide 7
18.18.1 Packetizing
The first duty of the network layer is definitely packetizing: encapsulating the payload in a network-layer packet at the source and decapsulating the payload from the network-layer packet at the destination. In other words, one duty of the network layer is to carry a payload from the source to the destination without changing it or using it. The network layer is doing the service of a carrier such as the postal office, which is responsible for delivery of packages from a sender to a receiver without changing or using the contents.

## Slide 8
18.18.2 Routing and Forwarding
Other duties of the network layer, which are as important as the first, are routing and forwarding, which are directly related to each other.

## Slide 9
Figure 18.2: Forwarding process

## Slide 10
18.18.3 Other Services
Let us briefly discuss other services expected from the network layer.

## Slide 11
    18-2 PACKET SWITCHING
From the discussion of routing and forwarding in the previous section, we infer that a kind of switching occurs at the network layer. A router, in fact, is a switch that creates a connection between an input port and an output port (or a set of output ports), just as an electrical switch connects the input to the output to let electricity flow.

## Slide 12
18.2.1 Datagram Approach
When the Internet started, to make it simple, the network layer was designed to provide a connectionless service in which the network-layer protocol treats each packet independently, with each packet having no relationship to any other packet. The idea was that the network layer is only responsible for delivery of packets from the source to the destination. In this approach, the packets in a message may or may not travel the same path to their destination. Figure 18.3 shows the idea..

## Slide 13
Figure 18.3: A connectionless packet-switched network

## Slide 14
Figure 18.4: Forwarding process in a router when used in a
connectionless network

## Slide 15
18.2.2 Virtual-Circuit Approach
In a connection-oriented service (also called virtual-circuit approach), there is a relationship between all packets belonging to a message. Before all datagrams in a message can be sent, a virtual connection should be set up to define the path for the datagrams. After connection setup, the datagrams can all follow the same path. In this type of service, not only must the packet contain the source and destination addresses, it must also contain a flow label, a virtual circuit identifier that defines the virtual path the packet should follow.

## Slide 16
Figure 18.5: A virtual-circuit packet-switched network

## Slide 17
Figure 18.6: Forwarding process in a router when used in a virtual
circuit network

## Slide 18
Figure 18.7: Sending request packet in a virtual-circuit network

## Slide 19
Figure 18.8: Sending acknowledgments in a virtual-circuit network

## Slide 20
Figure 18.9: Flow of one packet in an established virtual circuit

## Slide 21
    18-3 NETWORK-LAYER PERFORMANCE
The upper-layer protocols that use the service of the network layer expect to receive an ideal service, but the network layer is not perfect. The performance of a network can be measured in terms of delay, throughput, and packet loss. Congestion control is an issue that can improve the performance.

## Slide 22
18.3.1 Delay
All of us expect instantaneous response from a network, but a packet, from its source to its destination, encounters delays. The delays in a network can be divided into four types: transmission delay, propagation delay, processing delay, and queuing delay.
Total Delay = (N+1) ( (n) ()

## Slide 23
18.3.2 Throughput
Throughput at any point in a network is defined as the number of bits passing through the point in a second, which is actually the transmission rate of data at that point. In a path from source to destination, a packet may pass through several links (networks), each with a different transmission rate. How, then, can we determine the throughput of the whole path? To see the situation, assume that we have three links, each with a different transmission rate, as shown in Figure 18.10.

## Slide 24
Figure 18.10: Throughput in a path with three links in a series

## Slide 25
Figure 18.11: A path through the Internet backbone

## Slide 26
Figure 18.12: Effect of throughput in shared links

## Slide 27
18.3.3 Packet Loss
Another issue that severely affects the performance of communication is the number of packets lost during transmission. When a router receives a packet while processing another packet, the received packet needs to be stored in the input buffer waiting for its turn. A router, however, has an input buffer with a limited size. A time may come when the buffer is full and the next packet needs to be dropped. The effect of packet loss on the Internet network layer is that the packet needs to be resent, which in turn may create overflow and cause more packet loss.

## Slide 28
18.3.4 Congestion Control
Congestion control is a mechanism for improving performance. In Chapter 23, we will discuss congestion at the transport layer. Although congestion at the network layer is not explicitly addressed in the Internet model, the study of congestion at this layer may help us to better understand the cause of congestion at the transport layer and find possible remedies to be used at the network layer. Congestion at the network layer is related to two issues, throughput and delay, which we discussed in the previous section.

## Slide 29
Figure 18.13. Packet delay and throughput as functions of load

## Slide 30
Figure 18.14: Backpressure method for alleviating congestion

## Slide 31
Figure 4.15: Choke packet

## Slide 32
    18-4 IPv4 ADDRESSES
The identifier used in the IP layer of the TCP/IP protocol suite to identify the connection of each device to the Internet is called the Internet address or IP address. An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a host or a router to the Internet. The IP address is the address of the connection, not the host or the router.

## Slide 33
18.4.1 Address Space
A protocol like IPv4 that defines addresses has an address space. An address space is the total number of addresses used by the protocol. If a protocol uses b bits to define an address, the address space is 2b because each bit can have two different values (0 or 1). IPv4 uses 32-bit addresses, which means that the address space is 4,294,967,296 (more than four billion). If there were no restrictions, more than 4 billion devices could be connected to the Internet.

## Slide 34
Figure 18.16: Three different notations in IPv4 addressing

## Slide 35
Figure 18.17: Hierarchy in addressing

## Slide 36
18.4.2 Classful Addressing
When the Internet started, an IPv4 address was designed with a fixed-length prefix, but to accommodate both small and large networks, three fixed-length prefixes were designed instead of one (n = 8, n = 16, and n = 24). The whole address space was divided into five classes (class A, B, C, D, and E), as shown in Figure 18.18. This scheme is referred to as classful addressing. Although classful addressing belongs to the past, it helps us to understand classless addressing, discussed later.

## Slide 37
Figure 18.18: Occupation of the address space in classful addressing

## Slide 38
18.4.3 Classless Addressing
With the growth of the Internet, it was clear that a larger address space was needed as a long-term solution. The larger address space, however, requires that the length of IP addresses also be increased, which means the format of the IP packets needs to be changed. Although the long-range solution has already been devised and is called IPv6, a short-term solution was also devised to use the same address space but to change the distribution of addresses to provide a fair share to each organization. The short-term solution still uses IPv4 addresses, but it is called classless addressing.

## Slide 39
Figure 18.19: Variable-length blocks in classless addressing

## Slide 40
Figure 18.20: Slash notation (CIDR)

## Slide 41
Figure 18.21: Information extraction in classless addressing
Set all suffix bits
to 1s
Set all suffix bits
to 0s

## Slide 42
A classless address is given as 167.199.170.82/27. We can find the above three pieces of information as follows. The number of addresses in the network is 232− n = 25 = 32 addresses. The first address can be found by keeping the first 27 bits and changing the rest of the bits to 0s.
Example 18.1
The last address can be found by keeping the first 27 bits and changing the rest of the bits to 1s.
18.42

## Slide 43
We repeat Example 18.1 using the mask. The mask in dotted-decimal notation is 256.256.256.224 The AND, OR, and NOT operations can be applied to individual bytes using calculators and applets at the book website.
Example 18.2
18.43

## Slide 44
In classless addressing, an address cannot per se define the block the address belongs to. For example, the address 230.8.24.56 can belong to many blocks. Some of them are shown below with the value of the prefix associated with that block.
Example 18.3
18.44

## Slide 45
Figure 18.22: Network address

## Slide 46
An ISP has requested a block of 1000 addresses. Since 1000 is not a power of 2, 1024 addresses are granted. The prefix length is calculated as n = 32 − log21024 = 22. An available block, 18.14.12.0/22, is granted to the ISP. It can be seen that the first address in decimal is 302,910,464, which is divisible by 1024.
Example 18.4
18.46

## Slide 47
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.
Example 18.5
Solution
There are 232– 24 = 256 addresses in this block. The first address is 14.24.74.0/24; the last address is 14.24.74.255/24. To satisfy the third requirement, we assign addresses to subblocks, starting with the largest and ending with the smallest one.
18.47

## Slide 48
a. The number of addresses in the largest subblock, which requires 120 addresses, is not a power of 2. We allocate 128 addresses. The subnet mask for this subnet can be found as n1 = 32 − log2 128 = 25. The first address in this block is 14.24.74.0/25; the last address is 14.24.74.127/25.
b. The number of addresses in the second largest subblock, which requires 60 addresses, is not a power of 2 either. We allocate 64 addresses. The subnet mask for this subnet can be found as n2 = 32 − log2 64 = 26. The first address in this block is 14.24.74.128/26; the last address is 14.24.74.191/26.
Example 18.5 (continued)
18.48

## Slide 49
c. The number of addresses in the smallest subblock, which requires 10 addresses, is not a power of 2. We allocate 16 addresses. The subnet mask for this subnet can be found as n1 = 32 − log2 16 = 28. The first address in this block is 14.24.74.192/28; the last address is 14.24.74.207/28.
Example 18.5 (continued)
If we add all addresses in the previous subblocks, the result is 208 addresses, which means 48 addresses are left in reserve. The first address in this range is 14.24.74.208. The last address is 14.24.74.255. We don’t know about the prefix length yet. Figure 18.23 shows the configuration of blocks. We have shown the first address in each block.
18.49

## Slide 50
Figure 18.23: Solution to Example 4.5

## Slide 51
Figure 18.24 shows how four small blocks of addresses are assigned to four organizations by an ISP. The ISP combines these four blocks into one single block and advertises the larger block to the rest of the world. Any packet destined for this larger block should be sent to this ISP. It is the responsibility of the ISP to forward the packet to the appropriate organization. This is similar to routing we can find in a postal network. All packages coming from outside a country are sent first to the capital and then distributed to the corresponding destination.
Example 18.6
18.51

## Slide 52
Figure 18.24: Example of address aggregation

## Slide 53
18.4.4 DHCP
After a block of addresses are assigned to an organization, the network administration can manually assign addresses to the individual hosts or routers. However, address assignment in an organization can be done automatically using the Dynamic Host Configuration Protocol (DHCP). DHCP is an application-layer program, using the client-server paradigm, that actually helps TCP/IP at the network layer.

## Slide 54
Figure 18.25: DHCP message format

## Slide 55
Figure 18.26: Option format

## Slide 56
Figure 18.27: Operation of DHCP

## Slide 57
18.4.5 NAT
In most situations, only a portion of computers in a small network need access to the Internet simultaneously. A technology that can provide the mapping between the private and universal addresses, and at the same time support virtual private networks, which we discuss in Chapter 32, is Network Address Translation (NAT). The technology allows a site to use a set of private addresses for internal communication and a set of global Internet
addresses (at least one) for communication with the rest of the world.

## Slide 58
Figure 18.29: NAT

## Slide 59
Figure 18.30: Address translation
18.59

## Slide 60
Figure 18.31: Translation

## Slide 61
Table 18.1: Five-column translation table
18.61

## Slide 62
    18-5 FORWARDING OF IP PACKETS
We discussed the concept of forwarding at the network layer earlier in this chapter. In this section, we extend the concept to include the role of IP addresses in forwarding. As we discussed before, forwarding means to place the packet in its route to its destination.

## Slide 63
Figure 18.32: Simplified forwarding module in classless address

## Slide 64
Make a forwarding table for router R1
Example 18.7
18.64

## Slide 65
Show the forwarding process if a packet arrives at R1 in Figure 18.33 with the destination address 180.70.65.140
Example 18.9
Solution
The router performs the following steps:
18. The first mask (/26) is applied to the destination address. The result is 180.70.65.128, which does not match the corresponding network address.
2. The second mask (/25) is applied to the destination address. The result is 180.70.65.128, which matches the corresponding network address. The next-hop address and the interface number m0 are extracted for forwarding the packet (see Chapter 5).
18.65

## Slide 66
Figure 18.34: Address aggregation

## Slide 67
Figure 18.35: Longest mask matching

## Slide 68
As an example of hierarchical routing, let us consider Figure 18.36. A regional ISP is granted 16,384 addresses 120.14.64.0/18. The regional ISP has decided to divide this block into 4 subblocks, each with 4096 addresses. Three of these subblocks are assigned to three local ISPs, the second subblock is reserved for future use. Local ISP1 needs to divide its block of addresses into 8 small ISPs each having 512 addresses.
Example 18.10
18.68

## Slide 69
Figure 18.35: Hierarchical routing with ISPs

## Slide 70
An ISP is granted the block 16.12.64.0/20. The ISP needs to allocate addresses for 8 organizations, each with 256 addresses.
  Find the number and range of addresses in the ISP block.
  Find the range of addresses for each organization and the range of unallocated addresses.
P18-1
18.70