## Slide 1
11.<number>
Chapter 11
Data Link Control
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: <number>

## Slide 2
11.<number>
Data Link Control
Functions of the data link layer include:
  Error Detection & Correction
  Data Link Control: Design & procedures for node-to-node communication (flow and error control)
  Media Access Control: How to share the link.
Data Link Control functions include:
  Framing
  Flow and error control
  Protocols implemented in software to provide smooth and reliable transmission of frames between nodes.
Notes: <number>

## Slide 3
11.<number>
11-1-1 FRAMING
The data link layer packs bits into frames, and adds sender and destination addresses to each frame so that each frame is distinguishable from another.
Fixed-Size Framing Variable-Size Framing
Topics discussed in this section:
Notes: <number>

## Slide 4
11.<number>
Types of Frames
Frames could be of fixed or variable size.
In a fixed-size framing, there is no need to define boundaries of the frames, the size itself can be used as a delimiter. e.g. ATM
In variable-size framing (discussed in this chapter), we need a way to define the end of the frame and the beginning of the next. Two approaches were used for this purpose:
  Character-Oriented
  Bit-Oriented
Notes: <number>

## Slide 5
11.<number>
Character-Oriented Protocol
Data to be carried are 8-bit characters from a coding system such as ASCII.
Flag is an 8-bit that is added to the beginning and the end of a frame to separate it from next and previous frames.
Header is a multiple of 8-bit characters that carries the source and destination addresses.
Trailer is also a multiple of 8-bit characters that carries error detection and correction redundant bits.
Notes: <number>

## Slide 6
11.<number>
Character Stuffing & Unstuffing
In order not to confuse a flag with a data character, Character Stuffing (or Byte Stuffing) is used.
In Character Stuffing, a special character (ESC) is added to the data section of the frame when there is a character with the same pattern as the flag or the special character.
Notes: <number>

## Slide 7
11.<number>
Bit-Oriented Protocol
Data section of a frame is a sequence of bits to be interpreted by the upper layer.
Flag is a special 8-bit pattern 01111110 that is added to the beginning and the end of a frame to separate it from next and previous frames.
Header and Trailer are needed as in Character-Oriented Protocol.
Notes: <number>

## Slide 8
11.<number>
Bit Stuffing & Unstuffing
Bit stuffing is the process of adding one extra 0 whenever five consecutive 1s follow a 0 in the data, so that the receiver does not mistake the pattern 0111110 for a flag.
Notes: <number>

## Slide 9
11.<number>
11-1-2 FLOW AND ERROR CONTROL
The most important responsibilities of the data link layer are flow control and error control. Collectively, these functions are known as data link control.
Flow Control: Refers to a set of procedures used to restrict the amount of data that the sender can send before waiting for acknowledgment. Error Control: Error control in the data link layer is based on Automatic Repeat Request (ARQ), which is the retransmission of data.
Topics discussed in this section:
Notes: <number>

## Slide 10
11.<number>
11-2 Data Link Protocls
Notes: <number>

## Slide 11
11.<number>
11-2 Data Link Protocols
Let us first assume we have an ideal channel in which no frames are lost, duplicated, or corrupted. We introduce two protocols for this type of channel.
Simplest Protocol Stop-and-Wait Protocol
Topics discussed in this section:
Notes: <number>

## Slide 12
11.<number>
Simplest Protocol
No flow or error control.
Receiver can immediately handle any frame it receives, process it and pass it to above layers.
Receiver can never be overwhelmed with incoming frames.
The sender sends a sequence of frames without even thinking about the receiver.
Notes: <number>

## Slide 13
11.<number>
Stop-and-Wait Protocol
When data frames arrive at the receiver site faster than they can be processed, it needs to tell the sender to slow down.
In Stop-and-Wait Protocol sender sends one frame, stops until it receives Acknowledgment Frame (ACK) from receiver, then sender proceeds with sending next frame.
Notes: <number>