## Slide 1
Chapter 10
Error
Detection
And
Correction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: <number>

## Slide 2
Chapter 10: Outline
10.1 INTRODUCTION
10.2 BLOCK CODING
10.3 CYCLIC CODES
Notes: 10.#

## Slide 3
Chapter 10: Objective
The first section introduces types of errors, the concept of redundancy, and distinguishes between error detection and correction.
The second section discusses block coding. It shows how error can be detected using block coding and also introduces the concept of Hamming distance.
The third section discusses cyclic codes. It discusses a subset of cyclic code, CRC, that is very common in the data-link layer. The section shows how CRC can be easily implemented in hardware and represented by polynomials.
Notes: 10.#

## Slide 4
Chapter 10: Objective (continued)
The fourth section discusses checksums. It shows how a checksum is calculated for a set of data words. It also gives some other approaches to traditional checksum.
The fifth section discusses forward error correction. It shows how Hamming distance can also be used for this purpose. The section also describes cheaper methods to achieve the same goal, such as XORing of packets, interleaving chunks, or compounding high and low resolutions packets.
Notes: 10.#

## Slide 5
10.<number>
    10-1 INTRODUCTION
Let us first discuss some issues related, directly or indirectly, to error detection and correction.
Notes: 10.#

## Slide 6
10.<number>
10.10.1 Types of Errors
Whenever bits flow from one point to another, they are subject to unpredictable changes because of interference. This interference can change the shape of the signal. The term single-bit error means that only 1 bit of a given data unit (such as a byte, character, or packet) is changed from 1 to 0 or from 0 to 10. The term burst error means that 2 or more bits in the data unit have changed from 1 to 0 or from 0 to 10. Figure 10.1 shows the effect of a single-bit and a burst error on a data unit.
Notes: 10.#

## Slide 7
10.<number>
Figure 10.1: Single-bit and burst error
Notes: 10.#

## Slide 8
10.<number>
10.10.2 Redundancy
The central concept in detecting or correcting errors is redundancy. To be able to detect or correct errors, we need to send some extra bits with our data. These redundant bits are added by the sender and removed by the receiver. Their presence allows the receiver to detect or correct corrupted bits.
Notes: 10.#

## Slide 9
10.<number>
10.10.3 Detection versus Correction
The correction of errors is more difficult than the detection. In error detection, we are only looking to see if any error has occurred. The answer is a simple yes or no. We are not even interested in the number of corrupted bits. A single-bit error is the same for us as a burst error. In error correction, we need to know the exact number of bits that are corrupted and, more importantly, their location in the message.
Notes: 10.#

## Slide 10
10.<number>
10.10.4 Coding
Redundancy is achieved through various coding schemes. The sender adds redundant bits through a process that creates a relationship between the redundant bits and the actual data bits. The receiver checks the relationships between the two sets of bits to detect errors. The ratio of redundant bits to data bits and the robustness of the process are important factors in any coding scheme.
Notes: 10.#

## Slide 11
10.<number>
    10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords. How the extra r bits are chosen or calculated is something
we will discuss later.
Notes: 10.#

## Slide 12
10.<number>
10.2.1 Error Detection
How can errors be detected by using block coding? If the following two conditions are met, the receiver can detect a change in the original codeword.
10. The receiver has (or can find) a list of valid codewords.
2. The original codeword has changed to an invalid one.
Notes: 10.#

## Slide 13
10.<number>
Figure 10.2: Process of error detection in block coding
10.<number>
Notes: 10.#

## Slide 14
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords. Later, we will see how to derive a codeword from a dataword.
Example 10.1
Table 10.1: A code for error detection in Example 10.1
10.<number>
Notes: <number>

## Slide 15
Let us find the Hamming distance between two pairs of words.
Example 10.2
10.<number>
Notes: <number>

## Slide 16
10.<number>
Figure 10.3: Geometric concept explaining dmin in error detection
Notes: 10.#

## Slide 17
The minimum Hamming distance for our first code scheme (Table 10.1) is 2. This code guarantees detection of only a single error. For example, if the third codeword (101) is sent and one error occurs, the received codeword does not match any valid codeword. If two errors occur, however, the received codeword may match a valid codeword and the errors are not detected.
Example 10.3
10.<number>
Table 10.1: A code for error detection in Example 10.1
Notes: <number>

## Slide 18
A code scheme has a Hamming distance dmin = 4. This code guarantees the detection of up to three errors (d = s + 1 or
s = 3).
Example 10.4
10.<number>
Notes: <number>

## Slide 19
The code in Table 10.1 is a linear block code because the result of XORing any codeword with any other codeword is a valid codeword. For example, the XORing of the second and third codewords creates the fourth one.
Example 10.5
10.<number>
Table 10.1: A code for error detection in Example 10.1
In our first code (Table 10.1), the numbers of 1s in the nonzero codewords are 2, 2, and 2. So the minimum Hamming distance is dmin = 2.
Notes: <number>

## Slide 20
Table 10.2: Simple parity-check code C(5, 4)
10.<number>
Notes: <number>

## Slide 21
10.<number>
Figure 10.4: Encoder and decoder for simple parity-check code
Notes: 10.#

## Slide 22
Let us look at some transmission scenarios. Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
Example 10.7
10.<number>
Notes: <number>

## Slide 23
10.<number>
    10-3 CYCLIC CODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword. For example, if 1011000 is a codeword and we cyclically left-shift, then 0110001 is also a codeword.
Notes: 10.#

## Slide 24
10.<number>
10.3.1 Cyclic Redundancy Check
We can create cyclic codes to correct errors. However, the theoretical background required is beyond the scope of this book. In this section, we simply discuss a subset of. cyclic codes called the cyclic redundancy check (CRC), which is used in networks such as LANs and WANs.
Notes: 10.#

## Slide 25
Table 10.3: A CRC code with C(7, 4)
10.<number>
Notes: <number>

## Slide 26
10.<number>
Figure 10.5: CRC encoder and decoder
Notes: 10.#

## Slide 27
10.<number>
Figure 10.6: Division in CRC encoder
Notes: 10.#

## Slide 28
10.<number>
Figure 10.7: Division in the CRC decoder for two cases
Notes: 10.#