## Slide 1
Chapter 3
Introduction
To
Physical
Layer
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
Chapter 3: Outline
3.1 DATA AND SIGNALS
3.2 PERIODIC ANALOG SIGNALS
3.3 DIGITAL SIGNALS
3.4 TRANSMISSION IMPAIRMENT
3.5 DATA RATE LIMITS
3.6 PERFORMANCE

## Slide 3
Chapter 3: Objective
The first section shows how data and signals can be either analog or digital. Analog refers to an entity that is continuous; digital refers to an entity that is discrete.
The second section shows that only periodic analog signals can be used in data communication. The section discusses simple and composite signals. The attributes of analog signals such as period, frequency, and phase are also explained.
The third section shows that only non-periodic digital signals can be used in data communication. The attributes of a digital signal such as bit rate and bit length are discussed. We also show how digital data can be sent using analog signals. Baseband and broadband transmission are also discussed in this section.

## Slide 4
Chapter 3: Objective (continued)
The fourth section is devoted to transmission impairment. The section shows how attenuation, distortion, and noise can impair a signal.
The fifth section discusses the data rate limit: how many bits per second we can send with the available channel. The data rates of noiseless and noisy channels are examined and compared.
The sixth section discusses the performance of data transmission. Several channel measurements are examined including bandwidth, throughput, latency, and jitter. Performance is an issue that is revisited in several future chapters.

## Slide 5
    3-1 DATA AND SIGNALS
Figure 3.1 shows a scenario in which a scientist working in a research company, Sky Research, needs to order a book related to her research from an online bookseller, Scientific Books.

## Slide 6
Figure 3.1: Communication at the physical layer

## Slide 7
3.1.1 Analog and Digital Data
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. For example, an analog clock that has hour, minute, and second hands gives information in a continuous form; the movements of the hands are continuous. On the other hand, a digital clock that reports the hours and the minutes will change suddenly from 8:05 to 8:06.

## Slide 8
3.1.2 Analog and Digital Signals
Like the data they represent, signals can be either analog or digital. An analog signal has infinitely many levels of intensity over a period of time. As the wave moves from value A to value B, it passes through and includes an infinite number of values along its path. A digital signal, on the other hand, can have only a limited number of defined values. Although each value can be any number, it is often as simple as 1 and 0.

## Slide 9
Figure 3.2: Comparison of analog and digital signals

## Slide 10
3.1.3 Periodic and Nonperiodic
A periodic signal completes a pattern within a measurable time frame, called a period, and repeats that pattern over subsequent identical periods. The completion of one full pattern is called a cycle. A nonperiodic signal changes without exhibiting a pattern or cycle that repeats over time. Both analog and digital signals.

## Slide 11
    3-2 PERIODIC ANALOG SIGNALS
Periodic analog signals can be classified as simple or composite. A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals. A composite periodic analog signal is composed of multiple sine waves.

## Slide 12
3.2.1 Sine Wave
The sine wave is the most fundamental form of a periodic analog signal. When we visualize it as a simple oscillating curve, its change over the course of a cycle is smooth and consistent, a continuous, rolling flow. Figure 3.3 shows a sine wave. Each cycle consists of a single arc above the time axis followed by a single arc below it.

## Slide 13
Figure 3.3: A sine wave

## Slide 14
Figure 3.4: Two signals with two different amplitudes

## Slide 15
Figure 3.5: Two signals with the same phase and frequency, but different amplitudes

## Slide 16
Table 3.1: Units of period and frequency

## Slide 17
3.2.2 Phase
The term phase, or phase shift, describes the position of the waveform relative to time 0. If we think of the wave as something that can be shifted backward or forward along the time axis, phase describes the amount of that shift. It indicates the status of the first cycle.

## Slide 18
Figure 3.6: Three sine waves with different phases

## Slide 19
A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example 3.6
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is

## Slide 20
3.2.3 Wavelength
Wavelength is another characteristic of a signal traveling through a transmission medium. Wavelength binds the period or the frequency of a simple sine wave to the propagation speed of the medium (see Figure 3.7).

## Slide 21
Figure 3.7: Wavelength and period

## Slide 22
3.2.4 Time and Frequency Domains
A sine wave is comprehensively defined by its amplitude, frequency, and phase. We have been showing a sine wave by using what is called a time domain plot. The time-domain plot shows changes in signal amplitude with respect to time (it is an amplitude-versus-time plot). Phase is not explicitly shown on a time-domain plot.

## Slide 23
Figure 3.8: The time-domain and frequency-domain plots of a sine wave

## Slide 24
Figure 3.9: The time domain and frequency domain of three sine waves

## Slide 25
3.2.5 Composite Signals
So far, we have focused on simple sine waves. Simple sine waves have many applications in daily life. We can send a single sine wave to carry electric energy from one place to another. For example, the power company sends a single sine wave with a frequency of 60 Hz to distribute electric energy to houses and businesses. As another example, we can use a single sine wave to send an alarm to a security center when a burglar opens a door or window in the house. In the first case, the sine wave is carrying
energy; in the second, the sine wave is a signal of danger.

## Slide 26
Figure 3.10: A composite periodic signal

## Slide 27
Figure 3.11: Decomposition of a composite periodic signal

## Slide 28
Figure 3.12: Time and frequency domain of a non-periodic signal

## Slide 29
3.2.6 Bandwidth
The range of frequencies contained in a composite signal is its bandwidth. The bandwidth is normally a difference between two numbers. For example, if a composite signal contains frequencies between 1000 and 5000, its bandwidth is 5000 − 1000, or 4000.

## Slide 30
Figure 3.13: The bandwidth of periodic and nonperiodic composite
signals

## Slide 31
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Example 3.10
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then

## Slide 32
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Example 3.11
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.15).

## Slide 33
Figure 3.15: The bandwidth for example 3.11

## Slide 34
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Example 3.12
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.16 shows the frequency domain and the bandwidth.

## Slide 35
    3-3 DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level. Figure 3.17 shows two signals, one with two levels
and the other with four.

## Slide 36
Figure 3.17: Two digital signals: one with two signal levels and the
other with four signal levels

## Slide 37
3.3.1 Bit Rate
Most digital signals are nonperiodic, and thus period and frequency are not appropriate characteristics. Another term—bit rate (instead of frequency)—is used to describe digital signals. The bit rate is the number of bits sent in 1s, expressed in bits per second (bps). Figure 3.17 shows the bit rate for two signals.

## Slide 38
Assume we need to download text documents at the rate of 100 pages per second. What is the required bit rate of the channel?
Example 3.18
Solution

## Slide 39
3.3.2 Bit Length
We discussed the concept of the wavelength for an analog signal: the distance one cycle occupies on the transmission medium. We can define something similar for a digital signal: the bit length. The bit length is the distance one bit occupies on the transmission medium.

## Slide 40
3.3.3 Digital As Composite Analog
Based on Fourier analysis (See Appendix E), a digital signal is a composite analog signal. The bandwidth is infinite, as you may have guessed. We can intuitively come up with this concept when we consider a digital signal. A digital signal, in the time domain, comprises connected vertical and horizontal line segments. A vertical line in the time domain means a frequency of infinity: a horizontal line in the time domain means a frequency of zero. Going from a frequency of zero to a frequency of infinity implies all frequencies in between are part of the domain.

## Slide 41
Figure 3.18: The time and frequency domains of periodic and
nonperiodic digital signals

## Slide 42
    3-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect. The imperfection causes signal impairment. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium. What is sent is not what is received. Three causes of impairment are attenuation, distortion, and noise (see Figure 3.26).

## Slide 43
Figure 3.26: Causes of impairment

## Slide 44
3.4.1 Attenuation
Attenuation means a loss of energy. When a signal, simple or composite, travels through a medium, it loses some of its energy in overcoming the resistance of the medium. That is why a wire carrying electric signals gets warm, if not hot, after a while. Some of the electrical energy in the signal is converted to heat. To compensate for this loss, amplifiers are used to amplify the signal. Figure 3.27 shows the effect of attenuation and amplification..

## Slide 45
Figure 3.27: Attenuation and amplification

## Slide 46
3.4.2 Distortion
Distortion means that the signal changes its form or shape. Distortion can occur in a composite signal made of different frequencies. Each signal component has its own propagation speed (see the next section) through a medium and, therefore, its own delay in arriving at the final destination. Differences in delay may create a difference in phase if the delay is not exactly the same as the period duration.

## Slide 47
Figure 3.29: Distortion

## Slide 48
3.4.3 Noise
Noise is another cause of impairment. Several types of noise, such as thermal noise, induced noise, crosstalk, and impulse noise, may corrupt the signal. Thermal noise is the random motion of electrons in a wire, which creates an extra signal not originally sent by the transmitter. Induced noise comes from sources such as motors. Crosstalk is the effect of one wire on the other.

## Slide 49
Figure 3.30: Noise

## Slide 50
Figure 3.31: Two cases of SNR: a high SNR and a low SNR

## Slide 51
    3-6 PERFORMANCE
Up to now, we have discussed the tools of transmitting data (signals) over a network and how the data behave. One important issue in networking is the performance of the network—how good is it?

## Slide 52
3.6.1 Bandwidth and Throughput
One characteristic that measures network performance is bandwidth. However, the term can be used in two different contexts with two different measuring values: bandwidth in hertz and bandwidth in bits per second.
The throughput is a measure of how fast we can actually send data through a network. Although, at first glance, bandwidth in bits per second and throughput seem the same, they are different. A link may have a bandwidth of B bps, but we can only send T bps through this link with T always less than B.

## Slide 53
3.6.3 Latency (Delay)
The latency or delay defines how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source. We can say that latency is made of four components: propagation time, transmission time, queuing time and processing delay.

## Slide 54
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Example 3.44
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 55
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Example 3.45
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 56
What are the propagation time and the transmission time for a 2.5-KB (kilobyte) message if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Example 3.46
Solution
We can calculate the propagation and transmission time as
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time.

## Slide 57
3.6.4 Bandwidth-Delay Product
Bandwidth and delay are two performance metrics of a link. However, as we will see in this chapter and future chapters, what is very important in data communications is the product of the two, the bandwidth-delay product. Let us elaborate on this issue, using two hypothetical cases as examples.

## Slide 58
Figure 3.32: Filling the links with bits for Case 1

## Slide 59
Figure 3.33: Filling the pipe with bits for Case 2

## Slide 60
We can think about the link between two points as a pipe. The cross section of the pipe represents the bandwidth, and the length of the pipe represents the delay. We can say the volume of the pipe defines the bandwidth-delay product, as shown in Figure 3.34.
Example 3.48

## Slide 61
Figure 3.34: Concept of bandwidth-delay product