## Slide 1
Chapter 12
Media Access
Control
(MAC)
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
Chapter 5: Outline
12.1 RANDOM ACCESS
12.2 CONTROLLED ACCESS
12.3 CHANNELIZATION

## Slide 3
Chapter 12: Objective
The first section discusses random-access protocols. Four protocols, ALOHA, CSMA, CSMA/CD, and CSMA/CA, are described in this section. These protocols are mostly used in LANs and WANs, which we discuss in future chapters.
The second section discusses controlled-access protocols. Three protocols, reservation, polling, and token-passing, are described in this section. Some of these protocol are used in LANs, but others have some historical value.
The third section discusses channelization protocols. Three protocols, FDMA, TDMA, and CDMA are described in this section. These protocols are used in cellular telephony, which we discuss in Chapter 16.

## Slide 4
Figure 12.1: Taxonomy of multiple-access protocols

## Slide 5
    12-1 RANDOM ACCESS
In random-access or contention no station is superior to another station and
none is assigned control over another. At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send. This decision depends on the state of the medium (idle or busy).

## Slide 6
12.12.1 ALOHA
ALOHA, the earliest random access method, was developed at the University of Hawaii in early 1970. It was designed for a radio (wireless) LAN, but it can be used on any shared medium. It is obvious that there are potential collisions in this arrangement. The medium is shared between the stations. When a station sends data, another station may attempt to do so at the same time. The data from the two stations collide and become garbled.

## Slide 7
Figure 12.2: Frames in a pure ALOHA network

## Slide 8
Figure 12.3: Procedure for pure ALOHA protocol

## Slide 9
The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find Tp = (600 × 103) / (3 × 108) = 2 ms. For K = 2, the range of R is {0, 1, 2, 3}. This means that TB can be 0, 2, 4, or 6 ms, based on the outcome of the random variable R.
Example 12. 1
12.9

## Slide 10
Figure 12.4: Vulnerable time for pure ALOHA protocol

## Slide 11
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Solution
Average frame transmission time Tfr is 200 bits/200 kbps or 1 ms. The vulnerable time is 2 × 1 ms = 2 ms. This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the period (1 ms) that this station is sending.
Example 12.2
12.11

## Slide 12
Figure 12.5: Frames in a slotted ALOHA network

## Slide 13
Figure 12.6: Vulnerable time for slotted ALOHA protocol

## Slide 14
12.12.2 CSMA
To minimize the chance of collision and, therefore, increase the performance, the CSMA method was developed. The chance of collision can be reduced if a station senses the medium before trying to use it. Carrier sense multiple access (CSMA) requires that each station first listen to the medium (or check the state of the medium) before sending. In other words, CSMA is based on the principle “sense before transmit” or “listen before talk.”

## Slide 15
Figure 12.7: Space/time model of a collision in CSMA

## Slide 16
Figure 12.8: Vulnerable time in CSMA

## Slide 17
Figure 12.9: Behavior of three persistence methods

## Slide 18
Figure 12.10: Flow diagram for three persistence methods

## Slide 19
12.12.3 CSMA/CD
The CSMA method does not specify the procedure following a collision. Carrier sense multiple access with collision detection (CSMA/CD) augments the algorithm to handle the collision.
In this method, a station monitors the medium after it sends a frame to see if the transmission was successful. If so, the station is finished. If, however, there is a collision, the frame is sent again.

## Slide 20
Figure 12.11: Collision of the first bits in CSMA/CD

## Slide 21
Figure 12.12: Collision and abortion in CSMA/CD

## Slide 22
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal, as we see later) is 25.6 μs, what is the minimum size of the frame?
Solution
The minimum frame transmission time is Tfr = 2 × Tp = 512.2 μs. This means, in the worst case, a station needs to transmit for a period of 512.2 μs to detect the collision. The minimum size of the frame is 10 Mbps × 512.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet, as we will see later in the chapter.
Example 12. 5
12.22

## Slide 23
Figure 12.13: Flow diagram for the CSMA/CD

## Slide 24
Figure 12.14: Energy level during transmission, idleness, or collision

## Slide 25
12.12.4 CSMA/CA
Carrier sense multiple access with collision avoidance (CSMA/CA) was invented for wireless networks. Collisions are avoided through the use of CSMA/CA’s three strategies: the interframe space, the contention window, and acknowledgments, as shown in Figure 12.15. We discuss RTS and CTS frames later.

## Slide 26
Figure 12.15: Flow diagram for CSMA/CA

## Slide 27
Figure 12.16: Contention window

## Slide 28
Figure 12.17: CMACA and NAV

## Slide 29
    12-2 CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations. We discuss
three controlled-access methods.

## Slide 30
12.2.1 Reservation
In the reservation method, a station needs to make a reservation before sending data. Time is divided into intervals. In each interval, a reservation frame precedes the data frames sent in that interval.

## Slide 31
Figure 12.18: Reservation access method

## Slide 32
12.2.2 Polling
Polling works with topologies in which one device is designated as a primary station and the other devices are secondary stations. All data exchanges must be made through the primary device even when the ultimate destination is a secondary device. The primary device controls the link; the secondary devices follow its instructions. It is up to the primary
device to determine which device is allowed to use the channel at a given time.

## Slide 33
Figure 12.19: Select and poll functions in polling-access method

## Slide 34
12.2.3 Token Passing
In the token-passing method, the stations in a network are organized in a logical ring. In other words, for each station, there is a predecessor and a successor. The predecessor is the station which is logically before the station in the ring; the successor is the station which is after the station in the ring.

## Slide 35
Figure 12.20: Logical ring and physical topology in token-passing
access method

## Slide 36
    12-3 CHANNELIZATION
Channelization (or channel partition, as it is sometimes called) is a multiple-access
method in which the available bandwidth of a link is shared in time, frequency, or
through code, among different stations. In this section, we discuss three protocols: FDMA, TDMA, and CDMA.

## Slide 37
12.3.1 FDMA
In frequency-division multiple access (FDMA), the available bandwidth is divided into frequency bands. Each station is allocated a band to send its data. In other words, each band is reserved for a specific station, and it belongs to the station all the time. Each station also uses a bandpass filter to confine the transmitter frequencies. To prevent

## Slide 38
Figure 12.21: Frequency-division multiple access (FDMA)

## Slide 39
12.3.2 TDMA
In time-division multiple access (TDMA), the stations share the bandwidth of the channel in time. Each station is allocated a time slot during which it can send data. Each station transmits its data in its assigned time slot. Figure 12.22 shows the idea behind TDMA.

## Slide 40
Figure 12.22: Time-division multiple access (TDMA)

## Slide 41
12.3.3 CDMA
Code-division multiple access (CDMA) was conceived several decades ago. Recent advances in electronic technology have finally made its implementation possible. CDMA differs from FDMA in that only one channel occupies the entire bandwidth of the link. It differs from TDMA in that all stations can send data simultaneously; there is no timesharing.

## Slide 42
Figure 12.23: Simple idea of communication with code

## Slide 43
Figure 12.24: Chip sequences

## Slide 44
Figure 12.25: Data representation in CDMA

## Slide 45
Figure 12.26: Sharing channel in CDMA

## Slide 46
Figure 12.27: Digital signal created by four stations in CDMA

## Slide 47
Figure 12.28: Decoding of the composite signal for one in CDMA

## Slide 48
Prove that a receiving station can get the data sent by a specific sender if it multiplies the entire data on the channel by the sender’s chip code and then divides it by the number of stations.
Example 12.8
12.48