## Slide 1
Network Models
King Fahd University of Petroleum & Minerals
College of Computer Science & Engineering
Information & Computer Science Department
These slides are based on:
Chapter 2, Data Communications and Networking, 5th Edition
ICS 343
Fundamentals of Computer Networks

## Slide 2: Objectives
Describe layered tasks
Introduce the OSI model
Introduce the TCP/IP protocol suite

## Slide 3: OSI Model
Figure 2.2 Seven layers of the OSI model

## Slide 4: Layers Interaction
Figure 2.3 The interaction between layers in the OSI model

## Slide 5: Exchange between layers
Figure 2.4 An exchange using the OSI model

## Slide 6: Physical Layer
Deals with mechanical and electrical specifications of the interface and transmission media.
Defines the procedures and functions that physical devices and interfaces have to perform for transmission to occur. It is concerned about:
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate: Transmission rate – number of bits sent per second
  Synchronization of bits
  Line Configuration
  Physical Topology
  Transmission Mode
The physical layer is responsible for transmitting individual bits from one node to the next.

## Slide 7: Physical Layer
Figure 2.5 Physical layer

## Slide 8: Data Link Layer
Transforms the physical layer, a raw transmission facility, to a reliable link.
Makes the physical layer appear error-free to the upper layer (network layer).
  Framing: divide the stream of bits from network layer into frames
  Physical addressing
  Flow control: Prevent overwhelming the receiver.
  Error control: Detect and retransmit damaged or lost frames; Prevent duplication of frames; using trailer.
  Access control: Determine which device has control over the link at any given time.
The data link layer is responsible for transmitting frames from one node to next.

## Slide 9: Data Link Layer
Figure 2.6 Data link layer

## Slide 10: Example
A node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link. At the data link level this frame contains physical addresses in the header. These are the only addresses needed. The rest of the header contains other information needed at this level. The trailer usually contains extra bits needed for error detection:

## Slide 11: Hop-to-hop delivery
Figure 2.7 Hop-to-hop delivery

## Slide 12: Network Layer
Responsible for the source-to-destination delivery of a packet possibly across multiple networks.
Data link layer oversees the delivery of the packet between two systems on the same network.
Network layer ensures that each packet gets from its point of origin to its final destination.
  If two systems are connected to the same link, there is usually no need for a network layer.

## Slide 13: Network Layer
Figure 2.8 Network layer

## Slide 14: Network Layer
Logical addressing: Physical addressing in data link layer handles the addressing problem locally, this is why logical addressing is needed.
Routing: When independent networks or links are connected to create an internetwork (network of networks) or a large network, the connecting devices (called routers or switches) route or switch the packets to their final destination.

## Slide 15: Example
We want to send data from a node with network address A and physical address 10, located on one LAN, to a node with a network address P and physical address 95, located on another LAN. Because the two devices are located on different networks, we cannot use physical addresses only; the physical addresses only have local jurisdiction. What we need here are universal addresses that can pass through the LAN boundaries. The network (logical) addresses have this characteristic.

## Slide 16: Source-to-destination delivery
Figure 2.9 Source-to-destination delivery

## Slide 17: Transport Layer
Process-to-Process delivery
Network layer oversees host-to-destination delivery of individual packets, it does not recognize any relationship between those packets.
Ensures that the whole message arrives intact and in order, overseeing both error control and flow control at the process-to-process level.

## Slide 18: Transport Layer
The transport layer is responsible for delivery of a message from one process to another.
Port addressing: indicating a process
Segmentation and reassembly: divide into segments having sequence number.
Connection control: connection-oriented and connectionless
Flow control: end to end rather than across a single link.
Error control: End to end rather than across a single link. Sending transport layer makes sure that the entire message arrives at the receiving transport layer without error (damage, loss, or duplication).

## Slide 19: Transport Layer
Figure 2.10 Transport layer

## Slide 20: Process-to-process delivery
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 21: Example (cont)

## Slide 22: Session Layer
Session Layer
  Dialog control: Allows two systems to enter into a dialog, either half or full duplex.
    Terminal to mainframe is half duplex.
  Synchronization: Add check points (synchronization points) into a stream of data.

## Slide 23: Session Layer
Figure 2.12 Session layer

## Slide 24: Presentation Layer
Presentation layer
  Translation: Interoperability between different encoding methods.
  Encryption: For privacy.
  Compression: Reduces the number of bits contained in the information; useful in video, audio, …

## Slide 25: Presentation Layer

## Slide 26: Application Layer
Enables the user, whether human or software, to access the network.
Provides user interfaces and support for services such as electronic mail, remote file access and transfer, access to WWW, and so on.

## Slide 27: Summary of Layers
Figure 2.15 Summary of layers

## Slide 28: TCP/IP Protocol Suite
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.

## Slide 29: TCP/IP and OSI Models
Figure 2.16 TCP/IP and OSI model

## Slide 30: Addressing
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.

## Slide 31: Addresses in TCP/IP
Figure 2.17 Addresses in TCP/IP

## Slide 32: Addresses in TCP/IP
Figure 2.18 Relationship of layers and addresses in TCP/IP

## Slide 33: Note
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.

## Slide 34
The end
Important to do at home :
- read chapter 2 of the textbook