## Slide 1
Introduction to Networking
King Fahd University of Petroleum & Minerals
College of Computer Science & Engineering
Information & Computer Science Department
These slides are based on:
Chapter 1, Data Communications and Networking, 5th Edition
ICS 343
Fundamentals of Computer Networks

## Slide 2: Objectives
Introduction to Data Communication
Introduction to Networks
Introduction to the Internet
Protocols and Standards
1.<number>
Notes: 1.#

## Slide 3: Data Communications
1.<number>
The term telecommunication means communication at a distance. The word data refers to information presented in whatever form is agreed upon by the parties creating and using the data. Data communications are the exchange of data between two devices via some form of transmission medium such as a wire cable.
Notes: 1.#

## Slide 4: Five Components of Data Communications
1.<number>
Message: Data to be communicated
Sender & Receiver
Medium: Transmission medium is the physical path by which a message travels from sender to receiver
  Twisted-pair, coaxial cable, fiber optic cable or radio waves.
Protocol: Set of rules that govern data communications.
Notes: 1.#

## Slide 5: Effectiveness of Data Communication
1.<number>
Depends upon four fundamental characteristics:
  Delivery: Deliver data to the correct destination.
  Accuracy: Deliver the data accurately.
  Timeliness: Deliver data in a timely manner. Real-time transmission requires timely delivery [without significant delay].
  Jitter: Variations in packet arrival time.
Notes: 1.#

## Slide 6: Data Flow
1.<number>
Figure 1.2 Data flow (simplex, half-duplex, and full-duplex)
Notes: 1.#

## Slide 7: Networks
1.<number>
A network is a set of devices (often referred to as nodes) connected by communication links. A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network.
Notes: 1.#

## Slide 8: Network Criteria
Performance: Transit and response time.
  Transit time is the amount of time required for a message to travel from one device to another.
  Response time is the elapsed time between an inquiry and a response.
  Depends upon number of users, type of transmission medium, capabilities of hardware, efficiency of software.
Reliability: Measured by the frequency of failure, the time it takes a link to recover from a failure, and the network’s robustness in catastrophe.
Security: Protecting data from unauthorized access.
1.<number>

## Slide 9: Types of Connections
1.<number>
Figure 1.3 Types of connections: point-to-point and multipoint
Notes: 1.#

## Slide 10: Network Topology
1.<number>
Topology of a network is the geometric representation of the relationship of all the links and linking devices (nodes) to one another.
Notes: 1.#

## Slide 11: Mesh Topology
1.<number>
Every device has a dedicated point-to-point link to every other device.
Dedicated means that the link carries traffic only between the two devices it connects.
Adv: Guaranteed load, robust, privacy or security, fault identification and fault isolation is easier.
Disadv: amount of cabling, I/O ports, installation is difficult, more wiring w.r.t space, expensive hardware.
  Used at Backbone mostly.
Notes: 1.#

## Slide 12: Star Topology
1.<number>
Each device has a dedicated pt-to-pt link only to a central controller [Hub].
No direct connection or traffic.
Adv: less expensive, one link and one I/O port, easy to install and reconfigure, less cabling (but more than bus or ring), node failure will not affect others, fault identification is easier.
Disadv: Single point of failure.
Notes: 1.#

## Slide 13: Bus Topology
1.<number>
Multipoint: One cable acts as a backbone to link all the devices in a network.
Drop line: a connection running between the device and main cable.
Tap: a connector that either splices into the main cable or punctures the sheathing of the cable to create a contact with the metallic core.
Signal degrades due to energy being transformed into heat. So, there is limitation on the number of taps allowed.
Adv: easy to install, less cabling.
Disadv: Limit on number of taps and the distance between taps, difficult to identify fault, signal degradation, modification is difficult.
Notes: 1.#

## Slide 14: Ring Topology
1.<number>
Each device has a dedicated pt-to-pt connection only with the two devices on either side of it.
Each device incorporates a repeater.
When a device receives a signal intended for another device, its repeater regenerates the bits and passes them along.
Adv: Easy to install, fault isolation is easier, Signal circulates at all times (alarm alerts the problem and its location).
Disadv: Unidirectional traffic, in a simple ring; break in the ring can disable entire network.
Some systems have dual ring or switch capable of closing off the break.
Notes: 1.#

## Slide 15: Hybrid Topology
1.<number>
Figure 1.9 A hybrid topology: a star backbone with three bus networks
Notes: 1.#

## Slide 16: Isolated LAN
1.<number>
Figure 1.10 An isolated LAN connecting 12 computers to a hub in a closet
Notes: 1.#

## Slide 17: Categories of Networks
1.<number>
Size
Ownership
Distance it covers
Physical architecture
Notes: 1.#

## Slide 18: LAN
1.<number>
Privately owned
Links devices in single office, building or campus.
Limited to few kilometres.
Sharing of resources: Hardware or data.
Use a single transmission media.
Topology: Ring, bus, star.
Notes: 1.#

## Slide 19: LAN
1.<number>
Notes: 1.#

## Slide 20: MAN
1.<number>
Extend over an entire city.
Owned and operated by a private company.
Service provider.
Notes: 1.#

## Slide 21: WAN
1.<number>
Provides long-transmission of data, voice, image and video information over large geographic areas that may comprise a country, a continent or even the whole world.
WAN that is wholly owned and used by a single company is often referred to as an enterprise network.
Notes: 1.#

## Slide 22: Switched WAN and point-to-point WAN
1.<number>
Figure 1.11 WANs: a switched WAN and a point-to-point WAN
Notes: 1.#

## Slide 23: Hetergenous Network
1.<number>
Figure 1.12 A heterogeneous network made of four WANs and two LANs
Notes: 1.#

## Slide 24: The Internet
1.<number>
The Internet has revolutionized many aspects of our daily lives. It has affected the way we do business as well as the way we spend our leisure time. The Internet is a communication system that has brought a wealth of information to our fingertips and organized it for our use.
Notes: 1.#

## Slide 25: Organization of the Internet
1.<number>
Figure 1.13 Hierarchical organization of the Internet
Notes: 1.#

## Slide 26: Protocols and Standards
1.<number>
In this section, we define two widely used terms: protocols and standards. First, we define protocol, which is synonymous with rule. Then we discuss standards, which are agreed-upon rules.
Notes: 1.#

## Slide 27: Protocols and Standards
1.<number>
Protocols: set of rules that governs data communications.
A protocol defines what is communicated, how it is communicated and when it is communicated.
Syntax: it refers to the structure or format of data.
Semantics: it refers to the meaning of each section of bits
Timing: It refers to two characteristics; when and how much to send.
Standards: Provide guidelines to manufacturers.
de facto [by fact]
de jure [by law].
Notes: 1.#

## Slide 28: Standard Organizations
1.<number>
International Organization for Standardization (ISO)
International Telecommunication Union- Telecommunication Standards (ITU-T)
American National Standards Institute (ANSI)
Institute of Electrical and Electronics Engineers (IEEE)
Electronic Industries Association (EIA)
International Engineering Task Force (IETF)
Notes: 1.#

## Slide 29: Internet Standards and Drafts
1.<number>
Internet Standards
  Thoroughly tested specification that is useful to and adhered to by those who work with the Internet.
  Strict procedure and must be followed.
Internet draft
  Working document with no official status and 6-month life time.
  Upon recommendation from Internet authorities, can be published as a RFC [With number and made available to all interested parties.] RFC has maturity levels and are categorized according to their requirement levels.
Notes: 1.#

## Slide 30
The end
Important to do at home :
- read chapter 1 of the textbook